MATERIAL SAFETY DATA SHEET				Product Identifier: AUTO-SAN L.T.

SECTION 1 - PRODUCT IDENTIFICATION AND USE

Product Identifier:	AUTO-SAN L.T.

Product Use:		SANITIZER FOR AUTO DISHWASHING MACHINES

| Manufacturer: Nypower Industries Ltd Box 715 Okotoks, AB T1S 1A8 |  |  |
| --- | --- | --- |

EMERGENCY PHONE: (403) 995-2588

SECTION 2 - HAZARDOUS INGREDIENTS

| Hazardous Ingredients Sodium Hypochlorite |  | % 6 -12% |  | Cas Num. 7681-52-9 |  | LD50/LC50 of Ingredient Oral LD50 (Rat) 8200 mg/kg Dermal LD50 (Rabbit) 10000 mg/kg |
| --- | --- | --- | --- | --- | --- | --- |

SECTION 3 - PHYSICAL DATA

| Physical State: Liquid Vapour Pressure: 17.5 mm Hg @ 20 C Ph: 12.25 Boiling Point (C) N/A |  | Odour & Appearance: Chlorine/ Clear Green, Yellow Vapour Density: N/A Specific Gravity: N/A Freezing Point: -25 C |  | Evaporation Rate: N/A Coeff.Water/Oil: N/A Odour Threshold: N/A |
| --- | --- | --- | --- | --- |

SECTION 4 - FIRE AND EXPLOSION DATA

Flammability:			NO

If yes, under what conditions:	Not Flammable

Means of Extinguishing:		Use media appropriate for surrounding Fire

| Flashpoint & Method: N/A Autoignition Temp: N/A Explosion Data/Impact: N/A |  | Upper Flammable Limit: N/A Lower Flammable: N/A |  | Hazardous Comb.Products: Chlorine (Acid Contact) Sensitivity to Static Dis N/A |
| --- | --- | --- | --- | --- |

SECTION 5 - REACTIVITY DATA

Chemical Stability:		NO

If no, under what conditions:	Unstable above 40 C, Sunlight, contact with metals.

Incompatability:			Yes

Which Substances:		Acids, Ammonia, Oxidizeable metals, Urea, Nickel, Copper, Tin, Manganese, Iron.

Reactivity (under what conditions):	Acids

Hazardous Decomposition Products:	Chlorine

Product Identifier: AUTO-SAN L.T.

SECTION 6 - TOXICOLOGICAL PROPERTIES

Route of Entry:  Skin Contact: X       Skin Absorption:        Eye Contact: X       Inhalation: X     Ingestion: X

Effects of Overexposure (Acute and/or Chronic)

EYES: 	Direct contact may cause severe irritation and damage resulting in blindness.

SKIN: 	Prolonged or repeated contact may bleach skin or cause dermatitis.

INGESTION:	Causes burning in mouth and throat and severe abdominal pain, vomiting and diarrhea.

| Exposure Limits: Not Established Teratogenicity: No Evidence |  | Irritancy of Product: Eyes/Skin Reproductive Toxicity: None Known |  | Product Sensitization No Evidence Mutagenicity None Known |  | Carcinogenicity No Evidence Synergistic Products Not Available |
| --- | --- | --- | --- | --- | --- | --- |

SECTION 7 - PREVENTIVE MEASURES

Personal Protection Equipment:

Eye wash station and rinsing facilities

| Gloves (Specify) Rubber/Neoprene Footwear (Specify) Safety Shoes |  | Respirator (Specify) None Req'd Clothing (Specify) To Prevent Skin Contact |  | Eye (Specify) Chemical Goggles Other (Specify) Rubber Apron |
| --- | --- | --- | --- | --- |

Engineering Controls (Spec Ventilation, Enclosed Process)

General room ventilation is adequate

Leak and Spill Procedure

Dike & Contain. Collect and reuse if possible. Absorb with inert material and place in waste container. Small spills can be wiped or flushed to sewer. Do not allow runoff into public waterways.

Waste Disposal

Dispose of in manner approved by local regulations

Handling Procedures and Equipment

Close container tightly when not in use. Avoid transfer of product into container other than original.

Storage Requirements

Store in below 29 C and above freezing.  Keep out of reach of children. Keep out of sunlight.

Special Shipping Information

Hypochlorite solution. Corrosive liquid NOS, UN 1791 Class 8, PGIII. Protect from freezing

SECTION 8 - FIRST AID MEASURES

Specific Measures:

EYES:		Flush immediately with water for 30 minutes, lifting eyelids. Get medical attention.

SKIN:		Flush with large quantities of water. Remove contaminated footwear and clothing.

Ingestion: 	DO NOT induce vomiting. If conscious rinse mouth with water, and drink 1 glass of water to dilute. Get medical attention. Do not give anything by mouth to an unconscious person.

IN ALL CASES: If symptoms persist seek medical attention

SECTION 9 - PREPARATION DATE OF MSDS

Prepared By: Nypower Industries		Phone: (403) 995-2588					January 2010

No guarantee is made as to accuracy of the data or statement contained herein. While this information is furnished in good faith, and is accurate to the best of our knowledge, no warranty, expressed or implied, of merchantability, fitness or other use is made. This information is offered only for your consideration, investigation and verification. Nypower Industries ltd shall not in any event be liable for special, incidental or consequential damages connection with its publication. Likewise, no statement herein shall be construed as a permission or recommendation for the use of any product in a manner that might infringe on existing patents.