MATERIAL SAFETY DATA SHEET					Product Identifier: STEAM 2000

SECTION 1 - PRODUCT IDENTIFICATION AND USE

Product Identifier:	STEAM 2000

Product Use:		CARPET CLEANER

| Manufacturer: Nypower Industries Ltd Box 715 Okotoks, Alberta T1S 1A8 |  |  |
| --- | --- | --- |

EMERGENCY PHONE: (403) 995-2588

SECTION 2 - HAZARDOUS INGREDIENTS

| Hazardous Ingredients Disodium Metasilicate Sodium Tripolyphosphate Sodium Carbonate |  | % 2-5 2-5 1-3 |  | Cas Num. 6834-92-0 7758-29-4 497-19-8 |  | LD50/LC50 of Ingredient RTEC Oral LD50 Rat : 1153 mg/kg Oral LD50 Mouse : 770 mg/kg Oral LD50 (Rat) 3100 mg/kg Dermal LD50 (Rabbit) 7940 mg/kg Oral LD50 (Rat) 4090 mg/kg |
| --- | --- | --- | --- | --- | --- | --- |

SECTION 3 - PHYSICAL DATA

| Physical State: LIQUID Vapour Pressure: LIKE WATER Ph: 11.9 Boiling Point (C) 106 C |  | Odour & Appearance: SLIGHT/CLEAR Vapour Density: LIKE WATER Specific Gravity: 1.0750 Freezing Point: 0 C |  | Evaporation Rate: LIKE WATER Coeff.Water/Oil: NOT AVAILABLE Odour Threshold: NOT APPLICABLE |
| --- | --- | --- | --- | --- |

SECTION 4 - FIRE AND EXPLOSION DATA

Flammability:			NO

If yes, under what conditions:	NOT FLAMMABLE

Means of Extinguishing:		USE EXTINGUISHING MEDIA APPROPRIATE FOR SURROUNDING FIRE

| Flashpoint & Method: N/A Autoignition Temp: N/A Explosion Data/Impact: N/A |  | Upper Flammable Limit: N/A Lower Flammable: N/A |  | Hazardous Comb.Products: N/A Sensitivity to Static Dis N/A |
| --- | --- | --- | --- | --- |

SECTION 5 - REACTIVITY DATA

Chemical Stability:		YES

If no, under what conditions:	PRODUCT IS STABLE

Incompatability:			YES

Which Substances:		STRONG ACIDS AND OXIDIZERS

Reactivity (under what conditions):	CONTACT WITH STRONG ACIDS AND OXIDIZERS

Hazardous Decomposition Products:	NONE KNOWN

Product Identifier: STEAM 2000

SECTION 6 - TOXICOLOGICAL PROPERTIES

Route of Entry:  Skin Contact: X       Skin Absorption:        Eye Contact: X       Inhalation:       Ingestion: X

Effects of Overexposure (Acute and/or Chronic)

EYES: 	Direct contact may result in irritation and redness

SKIN: 	Prolonged and repeated exposure may cause irritation, dryness

INGESTION:	May cause G.I. tract irritation, nausea, diarrhea

| Exposure Limits: NOT ESTABLISHED Teratogenicity: NO EVIDENCE |  | Irritancy of Product: EYE, SKIN Reproductive Toxicity: NO EVIDENCE |  | Product Sensitization NO EVIDENCE Mutagenicity NO EVIDENCE |  | Carcinogenicity NO EVIDENCE Synergistic Products NONE KNOWN |
| --- | --- | --- | --- | --- | --- | --- |

SECTION 7 - PREVENTIVE MEASURES

Personal Protection Equipment:

EYE WASH STATION AND RINSING FACILITIES

| Gloves (Specify) RUBBER (PROLONGED EXPOSURE) Footwear (Specify) SAFETY SHOES |  | Respirator (Specify) NOT REQUIRED Clothing (Specify) AS REQ'D TO PREVENT SKIN CONTACT |  | Eye (Specify) SAFETY GLASSES Other (Specify) |
| --- | --- | --- | --- | --- |

Engineering Controls (Spec Ventilation, Enclosed Process etc)

USE IN VENTILATED AREA IF POSSIBLE

Leak and Spill Procedure

STOP SPILL AT SOURCE. DIKE AND CONTAIN. COLLECT AND RE-USE. DO NOT ALLOW RUNOFF INTO PUBLIC WATERWAYS

Waste Disposal

DISPOSE OF IN ACCORDANCE WITH LOCAL REGULATIONS

Handling Procedures and Equipment

CLOSE CONTAINER WHEN NOT IN USE. AVOID TRANSFER OF PRODUCT. WASH THOROUGHLY AFTER HANDLING

Storage Requirements

STORE IN COOL DRY AREA. KEEP AWAY FROM CHILDREN

Special Shipping Information

DO NOT FREEZE

SECTION 8 - FIRST AID MEASURES

Specific Measures:

EYES:		FLUSH EYES IMMEDIATELY WITH WATER FOR 15 MINUTES

SKIN:		FLUSH THOROUGHLY WITH WATER, REMOVE CONTAMINATED CLOTHING AND FOOTWEAR

Inhalation:	MOVE VICTIM TO FRESH AIR AND REST

Ingestion: 	DO NOT INDUCE VOMITING. RINSE MOUTH WITH WATER AND DRINK LOTS OF WATER OR MILK THEN GIVE DILUTE VINEGAR, LEMON OR ORANGE JUICE.

IN ALL CASES: If symptoms persist seek medical attention

SECTION 9 - PREPARATION DATE OF MSDS

Prepared By: Nypower Industries		Phone: (403) 995-2588					Date: January 2010

No guarantee is made as to accuracy of the data or statement contained herein. While this information is furnished in good faith, and is accurate to the best of our knowledge, no warranty, expressed or implied, of merchantability, fitness or other use is made. This information is offered only for your consideration, investigation and verification. Nypower Industries ltd shall not in any event be liable for special, incidental or consequential damages connection with its publication. Likewise, no statement herein shall be construed as a permission or recommendation for the use of any product in a manner that might infringe on existing patents.